## Slide 1: ENPM 664 Final Project: Router Exploitation
Group 5
Brandon Altvater Bhagvat Giri Jonathan Luck James Ng

## Slide 2: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 3: Team Introduction
Brandon Altvater
  BS in Computer Science and BA in Communications from Salisbury University. Worked in Defense Contracting for over 10 years. Worked on US Army defensive cyber operations for a year. Holds Sec+, CySA+, GWAPT, and working towards passing the OSCP.
Bhagvat Giri
  BS in Computer Engineering, from Vishwakarma Engineering College, India. Holds CEH and CEPT certificates with plans for the OSCP certification too. Has internship experience as a cybersecurity analyst. Participates in platforms like HackTheBox, TryHackMe, and HackerOne.
James Ng
  Application Security Engineer based in NJ working for payment-processing platform provider doing DevOps and interactive & dynamic application scan testing (IAST/DAST)
Jonathan Luck
  BS in Computer Science from University of California, San Diego. Currently doing cybersecurity stuff for the Department of Justice.

## Slide 4: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 5: Project summary
Extract the firmware off a home router (Wavlink WN530HG4 AC1200)
Remotely compromise the router
After compromising the router:
  Determine how to perform man-in-the-middle attacks to manipulate traffic
  Create a persistent backdoor
Perform Internet scans to determine how many devices are affected by our exploit(s)
Source: wavlink.com

## Slide 6: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 7: Background: What Is a Router?
A router is a device that forwards IP traffic between networks
  It determines if an IP destination is outside the LAN subnet and forwards it to an interface
  Crucially, home-routers also provide network address translation (NAT) while forwarding traffic. NAT allows non-routable IP addresses on the LAN to access public IPs transparently
Typically, a home-router allows devices in your home to connect to the Internet
Most home-routers nowadays will also provide Wi-Fi access
Designed on: visual-paradigm.com

## Slide 8: Background: What Is a Router? (cont.)
Home routers are typically resource constrained to cut down on manufacturing costs
  Many don’t have active cooling (fans), so thermal management also constrains how powerful the SoC can be
  Also driven by consumer usage patterns
    Very few people push 1Gbps sustained through a home router
ARM or MIPS
  Some business-grade routers are x86(-64), but home routers typically don’t need that much computing power
Most are running some Linux variant nowadays
  Lower development effort/costs, with a lot of useful open-source features/programs available
Many routers are white-label products
  Manufactured by one company
  Customized and branded by another

## Slide 9: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 10: Related work
Threat actors such as Sandworm have infected over 500,000 routers in over 50 countries to perform attacks that can collect internet traffic information, block traffic, and even render routers inoperable
Other attacks on routers have included:
  Ad injection
  Cryptomining
  Proxying
  Using router as a zombie in a botnet for DDoSing or other monetization
There is some published work on extracting firmware from routers, but none specific to this manufacturer
There was some vulnerability research published against Wavlinks, but those appeared to be against older firmware versions*
  See RCE section
Read our proposal’s background/related work section for sources and if you are interested in learning more

## Slide 11: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 12: Hardware Analysis
MT7620A
  MediaTek SoC designed for networking devices
  32-bit MIPS single-core processor
  “Network accelerator” supposedly has 2Gbps throughput
  Limited in RAM: 64MB max SDRAM and 256 MB of DDR2
    We must be judicious about our payloads
  Supports JTAG and UART(!)
    Likely ways to get some form of access
Source: an awful smartphone photographer

## Slide 13: Hardware Analysis (cont.)
UART
  Four through holes labeled TX/RX/GND/VCC
    TX: varies, but never goes above 3.3V
    RX: 0V
    GND: 0V
    VCC: 3.3V
  Safe to say this is 3.3V UART TTL
Before we get into craziness like trying to find the JTAG ports or sniffing the flash chips to extract the firmware, let’s just try seeing what output we get from the UART port
One extremely bad soldering job later…

## Slide 14: Hardware Analysis (cont.)
After stubbornly brute-forcing the baud rate instead of just using a logic analyzer…
U-Boot output!
  With the option to halt the boot process and get into a U-boot shell
  Prints out the address of the 0x40 byte U-Boot image header and the address + length of the firmware image
Only 64 MB of RAM 😕

## Slide 15: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 16: Firmware Extraction
Halt the boot process and start examining memory
A U-Boot image header
LZMA encoding
U-Boot header magic
LZMA header

## Slide 17: Firmware Extraction (cont.)
Let’s try extracting the whole firmware image through U-Boot.
  Use md.l so to group bytes into 4-byte chunks
    Saves 3 bytes of output per 4 bytes
Hexdump format means each byte is represented by at least 3: two hex digits and a printed representation
Add in the address, spaces between groups of bytes, and the newlines…
67 bytes per 16 bytes, or a ~4.2:1 ratio
Firmware is functionally 4.2 * 5.3 MB = 22MB
57600 baud is ~57kbps
Source: Nickelodeon

## Slide 18: Firmware Extraction (cont.)
Success!

## Slide 19: Firmware Extraction (cont.)
A few binwalks later… A root filesystem!

## Slide 20: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 21: Information Disclosure
Right now, our attack surface is limited to unauthenticated endpoints on the web interface and any other network applications the device is running
We want to expand that attack surface to include authenticated interfaces
CVE-2020-10973
  Unauthenticated settings export
    Still present in the latest firmware
  The device settings, including plaintext usernames and passwords, are encrypted using a static password
    Password is visible after unpacking the firmware
  Didn’t realize this was already publicly disclosed until after we had discovered it

## Slide 22: Information Disclosure (cont.)
Trigger the settings export
Collect the results
Decrypt it

## Slide 23: Information Disclosure (cont.)
We can use this technique to get access to the administrative web interface of the router
Now any authenticated RCE functionally becomes unauthenticated RCE

## Slide 24: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 25: Remote Code Execution
Given our lack of experience with writing MIPS buffer overflows, finding a shell injection would be one of the easiest ways in
Many of the cgi binaries have calls to system() and popen(), both of which are vulnerable to shell injections
  They also call do_system(), which just wraps system(), so these calls are also vulnerable

## Slide 26: Remote Code Execution (cont.)
How about in the “Ping Test” functionality in adm.cgi?
That was easy…

## Slide 27: Remote Code Execution (cont.)
Except someone published this vulnerability about one week after we found it
  Back to the drawing board

## Slide 28: Remote Code Execution (cont.)
Password change functionality, also in adm.cgi
If we make the injected command hang infinitely, we won’t actually change the password
Password we provide

## Slide 29: Password Change RCE Demo

## Slide 30: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 31: Man-in-the-Middle
Now that we have remote shell access, we can use the router to perform man-in-the-middle (MITM) attacks
Luckily, the router uses iptables instead of some proprietary routing/firewall code
We show that we can redirect HTTP traffic, but this could also be used to block/sinkhole traffic

## Slide 32: Man-in-the-Middle (cont.)
What is going on?
We are inserting a rule into the PREROUTING chain. This tells iptables to perform some action on a packet before it makes a routing decision
We then tell it to search for TCP/80 traffic going to 10.1.0.50
If it finds traffic that matches, we tell it to perform a destination NAT (DNAT) and rewrite the destination to be 10.0.0.70
  Responses from .70 will be transparently re-written to appear as if they came from .50
iptables -t nat -i br0 -I PREROUTING -p tcp --dport 80 -d 10.1.0.50 -j DNAT --to 10.1.0.70
Source: redhat.com

## Slide 33: MITM Demo

## Slide 34: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 35: Persistent Backdoor
The firmware doesn’t have cryptographic signatures, so we can just modify it, right?
  Firmware-mod-kit doesn’t work in this case
  Neither does manually unpacking and re-packing

## Slide 36: Persistent Backdoor (cont.)
If we can’t easily modify the firmware (which is in flash), how else can we store data persistently?
  The router stores user/system configurations in non-volatile RAM (NVRAM)
If we can find another buffer overflow/shell injection with how NVRAM variables are used, we can get a persistent(ish) backdoor
  Will survive a reboot and firmware update
  Won’t survive a factory reset
Parameters:
  Assume we have access to the system already
  Would preferably happen automatically, or is less effort to trigger than our existing RCE
Bad photography pt. 3
There are references to “flash” in the functions that deal with NVRAM
NVRAM takes forever (multiple seconds) to commit changes, also suggesting it is an emulation layer over flash
This is the only flash chip we found on the board

## Slide 37: Persistent Backdoor (cont.)
  How about the password check functionality in login.cgi?
    Password is salted and hashed on the client side before being sent to the router
    The router needs to hash the plaintext password with the same hash for comparison
      It does this by echoing the salt+password combo into md5sum as a shell command
    There’s probably also a buffer overflow in the strcpy/strcat, as salt is user-controlled, and NVRAM variables can be at least 500 bytes long
      But buffer overflows are hard
We need to craft a payload that closes the single quotes so we can run a shell command, then re-opens them so the command doesn’t fail

## Slide 38: Persistent Backdoor (cont.)
We are going to overwrite 4 NVRAM variables:
  Two will store the bind shell in a hex-encoded form
  One will store a script that will combine, decode, and write out the bind shell to a file. It will also write a simple shell script with an infinite loop to run the bind shell
  The password variable will store a shell injection that will run the script
Given we already have access from the previous RCE vulnerability, writing these NVRAM variables isn’t too hard
  The manufacturer uses command line utilities to get and set NVRAM values
    nvram_get 2860 Password and nvram_set 2860 Password abcd1234
Generate the bind shell with msfvenom, as that will produce a bind shell about 300 bytes long, much smaller than writing/compiling one ourselves
  msfvenom -p linux/mipsle/shell_bind_tcp RHOST=0.0.0.0 LPORT=45678 -f elf > bind_shell

## Slide 39: Persistent Backdoor (cont.)
What does this look like in practice?
Encoded bind shell
Script that decodes the bind shell and drops a script that runs it
Shell injection. Runs the value stored in DM_BA_SERVER_URL as a shell command
Original password so user can still log in. “Password” will evaluate to this

## Slide 40: Persistent Backdoor Demo

## Slide 41: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 42: Internet Survey
Some botnets have started to include IoT devices and home routers
Home routers are particularly easy to find, as they must have a public IP to route Internet traffic
We want to know if these RCE vulnerabilities (both the zero-day we found and previous, unpatched vulnerabilities) can be used to create a botnet
Zmap
  Scan a random set of IPv4s to find devices with TCP/80 exposed to the Internet
Zgrab
  Application-layer scanner that we use to make a request to the web interface of previously identified IPv4 hosts
    Request /cgi-bin/ExportAllSettings.sh
      The information disclosure/unauthenticated settings export URL

## Slide 43: Internet Survey
We performed 4 independent Zmap scans, finding ~527,000 unique hosts that have TCP/80 open
Followed up with Zgrab
  Only one host replied with a response suggesting it was a Wavlink router
Might have been a problem with our methodology, as we did not get as many hosts responding to TCP/80 as the authors of the original Zmap paper did
Even still, there are so few of these routers with exposed web interfaces that botnet creators probably won’t waste their time

## Slide 44: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 45: Conclusion
We were able to successfully extract the firmware from the Wavlink WN530HG4 AC1200 router and unpack the filesystem
We found multiple shell injections that provide remote code execution when chained with an information disclosure vulnerability
We found a method to store and execute a backdoor that survives reboots and firmware upgrades
We scanned a chunk of the IPv4 space and determine that Wavlink routers are unlikely to get added/turned into large botnets

## Slide 46: Agenda
Team introduction
Project summary
Background
Related work
Project results:
  Hardware analysis
  Firmware extraction
  Information disclosure
  Remote code execution
  Man-in-the-middle
  Persistent backdoor
  Internet Survey
Conclusion
Future work

## Slide 47: Future work
Look into the wctrls binary
  Listens on UDP port 36338 and appears to allow developers to enable telnetd at-will
    Some AES operations
    The latest firmware version removes telnetd, but keeps the wctrls binary
    There is a lot of copying buffers in memory. Potential for buffer overflows or bad TLV parsing
See how a factory reset actually works
  There appears to be a set of default NVRAM values stored in a file
    Can this file be manipulated so that our NVRAM backdoor survives a factory reset>
Allow users to change their password
  Because there is a strict comparison between the stored NVRAM plaintext password and the “old password” during a password change, our NVRAM backdoor prevents the user from changing their password
  Perhaps patch some binaries?
Investigate the discrepancy between our Zmap results and the original paper
Identify other routers using the same/similar chipsets, and see if they have shared implementations

## Slide 48: Thank You!
Questions?
  Email us:
    bgiri@umd.edu
    altvater@umd.edu
    jrluck@umd.edu
    jmhng18@umd.edu